#### Daniel Gooden
COSC240
Assignment 3
### Question 1
Total resources:
- Tape Drives: 8
- Modems: 9
- Printers: 8
Available resources:
- Tape Drives: 1
- Modems: 2
- Printers: 1
#### Need Matrix
Process	Tape Drives	Modems	Printers
P0	0	2	0
P1	0	3	5
P2	8	6	0
P3	2	1	1
P4	1	5	0

To determine a safe sequence we can see which process can currently be finished and allocate resources to it to lead to a safe state.
First we start with process P0. We can allocate the resources required (0, 2, 0) of the available resources. When the process completes we now have the following available resources:
- Tape Drives: 1
- Modems: 5
- Printers: 3
Next we check which process can run with the available resources. P4 is the only available process that can run so we allocate the resources (1, 5, 0) and after the process is finished we now have the following available resources:
- Tape Drives: 2
- Modems: 8
- Printers: 5
Again we check which processes can run. P1 is able to run so we allocate the resources (0, 3, 5) and after the process finishes we now have the following available resources:
- Tape Drives: 3
- Modems: 9
- Printers: 6
We return to P3 and allocate the needed resources (2, 1, 1) and after the process finishes we have the following resources available:
- Tape Drives: 8
- Modems: 9
- Printers: 6
We return to P2 and allocate the needed resources (8, 6, 0) and after the process finishes, we have completed all of the processes required.
The system is in a safe state and the safe sequence is P0 → P4 → P1 → P3 → P2
This ensures that all processes can complete without causing a deadlock.
### Question 2
Consider a process that refers to five pages: A, B, C, D, and E. The pages are referenced in the following order: C, A, C, E, B, D, C, C, B, D, E, A, E, B, D. Assuming memory is initially empty, and that no other processes are running, show the contents of each page frame for each step, along with any other necessary data (i.e. status of the referenced bit for second-chance and clock, process queue for second-chance, and the clock pointer for clock), and determine the number of page transfers during this sequence of references for the following page replacement algorithms and numbers of page frames:
  1. First-in, first-out:
    1. 3 page frames
Reference	Status	Frame	Queue
C	Page Fault	C, -, -	C
A	Page Fault	C, A, -	C, A
C	In memory	C, A, -	C, A
E	Page Fault	C, A, E	C, A, E
B	Page Fault	B, A, E	A, E, B
D	Page Fault	B, D, E	E, B, D
C	Page Fault	B, D, C	B, D, C
C	In memory	B, D, C	B, D, C
B	In memory	B, D, C	B, D, C
D	In memory	B, D, C	B, D, C
E	Page Fault	E, D, C	D, C, E
A	Page Fault	E, A, C	C, E, A
E	In memory	E, A, C	C, E, A
B	Page Fault	E, A, B	E, A, B
D	Page Fault	D, A, B	A, B, D

10 total page faults
    1. 4 page frames

Reference	Status	Frame	Queue
C	Page Fault	C, -, -, -	C
A	Page Fault	C, A, -, -	C, A
C	In Memory	C, A, -, -	C, A
E	Page Fault	C, A, E, -	C, A, E
B	Page Fault	C, A, E, B	C, A, E, B
D	Page Fault	D, A, E, B	A, E, B, D
C	Page Fault	D, C, E, B	E, B, D, C
C	In Memory	D, C, E, B	E, B, D, C
B	In Memory	D, C, E, B	E, B, D, C
D	In Memory	D, C, E, B	E, B, D, C
E	In Memory	D, C, E, B	E, B, D, C
A	Page Fault	D, C, A, B	B, D, C, A
E	Page Fault	D, C, A, E	D, C, A, E
B	Page Fault	B, C, A, E	C, A, E, B
D	Page Fault	B, D, A, E	A, E, B, D

10 total page faults
    1. 5 page frames

Reference	Status	Frame	Queue
C	Page Fault	C, -, -, -, -	C
A	Page Fault	C, A, -, -, -	C, A
C	In Memory	C, A, -, -, -	C, A
E	Page Fault	C, A, E, -, -	C, A, E
B	Page Fault	C, A, E, B, -	C, A, E, B
D	Page Fault	C, A, E, B, D	C, A, E, B, D
C	In Memory	C, A, E, B, D	C, A, E, B, D
C	In Memory	C, A, E, B, D	C, A, E, B, D
B	In Memory	C, A, E, B, D	C, A, E, B, D
D	In Memory	C, A, E, B, D	C, A, E, B, D
E	In Memory	C, A, E, B, D	C, A, E, B, D
A	In Memory	C, A, E, B, D	C, A, E, B, D
E	In Memory	C, A, E, B, D	C, A, E, B, D
B	In Memory	C, A, E, B, D	C, A, E, B, D
D	In Memory	C, A, E, B, D	C, A, E, B, D

5 total page faults
  1. Second-chance (assuming referenced bit is set when a page is first put in memory):
    1. 3 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -	C
A	Page Fault	C1, A1, -	C, A
C	In Memory	C1, A1, -	A, C
E	Page Fault	C1, A1, E1	A, C, E
B	Page Fault	C0, B1, E0	C, E, B
D	Page Fault	D1, B1, E0	E, B, D
C	Page Fault	D1, B1, C1	B, D, C
C	In Memory	D1, B1, C1	B, D, C
B	In Memory	D1, B1, C1	D, C, B
D	In Memory	D1, B1, C1	C, B, D
E	Page Fault	D0, B0, E1	B, D, E
A	Page Fault	D0, A1, E1	D, E, A
E	In Memory	D0, A1, E1	D, A, E
B	Page Fault	B1, A1, E1	A, E, B
D	Page Fault	B0, D1, E0	E, B, D

10 total page faults
    2. 4 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -, -	C
A	Page Fault	C1, A1, -, -	C, A
C	In Memory	C1, A1, -, -	A, C
E	Page Fault	C1, A1, E1, -	A, C, E
B	Page Fault	C1, A1, E1, B1	A, C, E, B
D	Page Fault	C0, D1, E0, B0	C, E, B, D
C	In Memory	C1, D1, E0, B0	E, B, D, C
C	In Memory	C1, D1, E0, B0	E, B, D, C
B	In Memory	C1, D1, E0, B1	E, D, C, B
D	In Memory	C1, D1, E0, B1	E, C, B, D
E	In Memory	C1, D1, E1, B1	C, B, D, E
A	Page Fault	A1, D0, E0, B0	B, D, E, A
E	In Memory	A1, D0, E1, B0	B, D, A, E
B	In Memory	A1, D0, E1, B1	D, A, E, B
D	In Memory	A1, D1, E1, B1	A, E, B, D

6 total page frames
    3. 5 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -, -, -	C
A	Page Fault	C1, A1, -, -, -	C, A
C	In Memory	C1, A1, -, -, -	A, C
E	Page Fault	C1, A1, E1, -, -	A, C, E
B	Page Fault	C1, A1, E1, B1, -	A, C, E, B
D	Page Fault	C1, D1, E1, B1, D1	A, C, E, B, D
C	In Memory	C1, D1, E1, B1, D1	A, E, B, D, C
C	In Memory	C1, D1, E1, B1, D1	A, E, B, D, C
B	In Memory	C1, D1, E1, B1, D1	A, E, D, C, B
D	In Memory	C1, D1, E1, B1, D1	A, E, C, B, D
E	In Memory	C1, D1, E1, B1, D1	A, C, B, D, E
A	In Memory	C1, D1, E1, B1, D1	C, B, D, E, A
E	In Memory	C1, D1, E1, B1, D1	C, B, D, A, E
B	In Memory	C1, D1, E1, B1, D1	C, D, A, E, B
D	In Memory	C1, D1, E1, B1, D1	C, A, E, B, D

5 total page faults
  1. Clock (assuming referenced bit is set when a page is first put in memory):
    1. 3 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -	C
A	Page Fault	C1, A1, -	C, A
C	In Memory	C1, A1, -	C, A
E	Page Fault	C1, A1, E1	C, A, E
B	Page Fault	B1, A0, E0	A, E, B
D	Page Fault	B1, D1, E0	E, B, D
C	Page Fault	B1, D1, C1	B, D, C
C	In Memory	B1, D1, C1	B, D, C
B	In Memory	B1, D1, C1	B, D, C
D	In Memory	B1, D1, C1	B, D, C
E	Page Fault	E1, D0, C0	D, C, E
A	Page Fault	E1, A1, C0	C, E, A
E	In Memory	E1, A1, C0	C, E, A
B	Page Fault	E1, A1, B1	E, A, B
D	Page Fault	D1, A0, B0	A, B, E

10 total page faults
    2. 4 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -, -	C
A	Page Fault	C1, A1, -, -	C, A
C	In Memory	C1, A1, -, -	C, A
E	Page Fault	C1, A1, E1, -	C, A, E
B	Page Fault	C1, A1, E1, B1	C, A, E, B
D	Page Fault	D1, A0, E0, B0	A, E, B, D
C	Page Fault	D1, C1, E0, B0	E, B, D, C
C	In Memory	D1, C1, E0, B0	E, B, D, C
B	In Memory	D1, C1, E0, B1	E, B, D, C
D	In Memory	D1, C1, E0, B1	E, B, D, C
E	In Memory	D1, C1, E1, B1	E, B, D, C
A	Page Fault	D0, C0, A1, B0	B, D, C, A
E	Page Fault	D0, C0, A1, E1	D, C, A, E
B	Page Fault	B1, C0, A1, E1	C, A, E, B
D	Page Fault	B1, D1, A1, E1	A, E, B, C

10 total page faults
    3. 5 page frames

Reference	Status	Frame w/ Ref Bit	Queue
C	Page Fault	C1, -, -, -, -	C
A	Page Fault	C1, A1, -, -, -	C, A
C	In Memory	C1, A1, -, -, -	C, A
E	Page Fault	C1, A1, E1, -, -	C, A, E
B	Page Fault	C1, A1, E1, B1, -	C, A, E, B
D	Page Fault	C1, A1, E1, B1, D1	C, A, E, B, D
C	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
C	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
B	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
D	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
E	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
A	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
E	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
B	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D
D	In Memory	C1, A1, E1, B1, D1	C, A, E, B, D

5 total page faults
### Question 3
Suppose an I-node can hold 11 direct block pointers, 5 indirect block pointers, and 3 double-indirect block pointers. Given a block size of 4KB, and 128-bit block numbers:
  1. What is the size (in bytes) of the smallest file that requires use of an indirect block pointer?
    11 direct block pointers x 4096 bytes = 45056 bytes
    The smallest size of file that requires an indirect block pointer is 45056 bytes + 1 byte = 45057 bytes.
  2. What is the size (in bytes) of the smallest file that requires use of a double-indirect block pointer?
    128 bit/ 8 = 16 bytes
    4096 bytes / 16 bytes per pointer = 256 pointers per indirect block
    4096 bytes * 256 pointers = 1048576 bytes or 1 Megabyte
    So the total size is going to be total amount of byte in the 11 direct block pointers (determined in part 1) + 5 * 1 MB + 1 byte.
    45056 bytes + 5 * 1 MB + 1 byte = 5287937 bytes
  3. What is the size (in bytes) of the largest file supported by this system?
     Each double indirect block points to 256 indirect blocks, and each of	those blocks points to 256 data blocks. So 1 double indirect block can	handle 256 * 1 MB = 256MB
     There is 3 double indirect block pointers, the total double indirect box	space is: 3 * 256MB = 768MB
     The total maximum file size:
     45056 bytes + 5MB + 768MB
     = 45056 bytes + 5242880 bytes + 805306368 bytes
     = 810594304 bytes
  4. What is the size (in bytes) of the largest file that would be supported by this system if it had 64-bit block numbers instead of 128-bit block numbers?
    The total size of the direct blocks remains unchanged. However the total size of the indirect and double indirect block pointers increases.
    The number of pointers per block becomes:
    4096 bytes / 8 bytes per pointer = 512 pointers
    Each indirect block can handle 512 pointers * 4096 bytes = 2MB
    Each double indirect block can handle 512 * 2MB = 1GB

    The total maximum file size with 64 bit blocks:
    45056 bytes + 5 * 2MB 3 * 1GB
    = 45056 bytes + 10485760 bytes + 3221225472 bytes
    = 3231756288 bytes
### Question 4
An application program takes time T to execute on a 10-computer cluster
  1. What is the effective speedup of running this application on the cluster rather than a single computer if 25% of T is spent running on all 10 computers, and the remaining time is spent running on a single computer?
  2. What is the effective speedup of running this application on the cluster rather than a single computer if 50% of T is spent running on all 10 computers, and the remaining time is spent running on a single computer?
  3. What is the effective speedup of running this application on the cluster rather than a single computer if 7% of T is spent running on all 10 computers, 34% of T is spent running on 7 computers, and the remaining time is spent running on a single computer?
  4. What is the effective speedup of running this application on the cluster rather than a single computer if 94% of T is spent running on all 10 computers,4% of T is spent running on 6 computers, and the remaining time is spent running on a single computer?
### Question 5
A computer virus is malicious software that replicates itself by modifying other programs to insert its own code. Antivirus software was initially designed to detect and remove computer viruses, but now also provides protection from other potential computer threats. Write a brief (approx. 500 words) history of the development of antivirus software, describing some of the techniques used by viruses that have required new methods of detection for antivirus software.